## Slide 1
FoxFrame
Window & Door Manufacturing
Optimization Platform
Profile Cutting • Glass Optimization • BOM Generation • Powered by WerkFox

## Slide 2
The Window Industry Problem
Indian window & door market: ₹45,000 Cr+ and growing 12% annually.
50,000+ fabricators, most using manual methods or expensive desktop software.
Expensive Software
LogiKal costs ₹5-15L upfront.
FeneVision is ₹15-75L+.
Small fabricators can't afford it.
Desktop Lock-in
Old software runs on 1 PC.
No cloud, no mobile access.
Data stuck on that machine.
Material Waste
8-15% aluminum bar waste.
10-18% glass sheet waste.
₹2-8L/year lost for mid-size shops.

## Slide 3
FoxFrame — Web-Based Window Manufacturing
₹49-199/month vs. ₹5-75L upfront for legacy tools
1D Profile Optimizer
Cut aluminum bars with minimal waste.
BFDH algorithm, kerf & end-trim aware.
Remnant tracking & reuse.
92-97% material utilization.
2D Glass Optimizer
Nest glass panels on jumbo sheets.
Guillotine-cut constraint (score & snap).
Coating direction support.
85-93% utilization.
Window Configurator
Define window type, dimensions,
mullions & transoms.
Auto-generate complete cut list.
Fixed, casement, sliding, tilt & turn.
BOM & Costing
Full bill of materials:
profiles, glass, hardware, gaskets.
Instant cost per window & per order.
Quotation generation.

## Slide 4
Aluminum Profile Cutting (1D)
The Core Problem:
50 windows need 400+ profile cuts from standard 6m bars.
How to cut them with minimum waste?
✓ Profile database — define codes, widths, weight/meter, price/meter
✓ Standard bar stock — 5000, 5800, 6000, 6500, 7000mm lengths
✓ Saw kerf handling — 3-5mm blade width per cut
✓ End trim — 10-25mm factory edge cleanup
✓ Angle cuts — 90° standard, 45° mitre, custom angles for shaped windows
✓ Remnant tracking — reuse leftover bar pieces from previous jobs
✓ Multi-order batching — combine orders for better optimization
✓ Bar labels — barcode/QR per cut piece for shop floor tracking

## Slide 5
Glass Sheet Optimization (2D)
Guillotine Constraint: all cuts must go edge-to-edge (score & snap).
Stock Sheet Size | Common Name
3210 × 2250 mm | Standard Jumbo
3210 × 2550 mm | Extended Jumbo
3660 × 2440 mm | North American Standard
4500 × 2500 mm | Oversized
6000 × 3210 mm | Super Jumbo (Curtain Wall)
Glass types supported:
• Clear float (4-12mm)
• Tinted / reflective
• Low-E coated
• Laminated
• Tempered
• Double/triple glazed IGU

## Slide 6
Supported Window & Door Types
Fixed
4 frame + 4 beads
Simple
Casement
8 main pieces
Medium
Tilt & Turn
8 pieces + hardware
Medium
Sliding
Frame + tracks + panels
Complex
Bi-fold
Multiple panels + track
Complex
Awning/Hopper
Similar to casement
Medium
+ Mullions & Transoms: vertical and horizontal dividers auto-generate additional cuts

## Slide 7
Why FoxFrame Wins
Feature | LogiKal / SchüCal | FeneVision | FoxFrame
Pricing | ₹5-15L upfront | ₹15-75L+ | ₹49-199/month
Deployment | Desktop install | On-premise/cloud | Cloud — instant access
Setup time | 3-6 months | 6-12 months | 10 minutes
Mobile access | No | Limited | Full responsive web
Multi-user | Per-seat license | Per-seat license | Team included
Updates | Annual fee | Annual fee | Always latest
Profile systems | Schüco only (SchüCal) | Any (complex setup) | Any (simple config)
Target | Large fabricators | Enterprise | SMB fabricators

## Slide 8
Modern Windows Deserve
Modern Software
Start with FoxFrame →
www.werkfox.com/foxframe
Part of the WerkFox Manufacturing Platform
FoxCut (Kitchens) + FoxFrame (Windows) + ERP + CRM